## Slide 1
Plasma-Based Particle Accelerators:
There’s Plenty of Room at the Bottom*
*Richard P. Feynman
1959 APS Meeting at CalTech
UT colloquium
October 16, 2013
100 µm
100 µm
~ c
Mike Downer
• TW  PW lasers
• MeV  GeV electrons
• VUV  hard x-ray
coherent
radiation
Wang et al., Nature Commun. 4, 1988 (2013)
Matlis et al., Nature Phys. 2, 749 (2006)
2006
record
< 0.5 mrad
< 5%
~ GV/cm
Notes: • My lecture demo is a 2” strand of my own hair, which represents the size of the accelerating channel of the GeV laser-plasma electron accelerators that I will tell you about today. These tiny accelerators can now do the job of a conventional accelerator > 1e4 x its size, or about 2 football fields long.
• The picture on the left shows a laboratory snapshot of a electron density (Langmuir) wave propagating at ~c thru a tenuous plasma in the wake of an intense laser pulse, inside which space charge fields reach ~GV/cm, > 1e4 x the breakdown field of a conventional metal accelerator.
• Plasma electrons captured within those fields can now reach energies as high as 2 GeV (see magnetically dispersed e- energy spectrum at the right) in a distance of only a few cm, an advance of 2x over the previous LPA record. Advances like this are spurred by the advent of PW lasers.
• But e- energy is only part of the story. The 2 GeV e- bunch has a record-setting angular divergence of < 0.5 mrad, and an energy spread (main part) of only ~ 5% which are critical to applications. Such features are the result of learning to observe, understand, manipulate and control PA accelerator structures on a µm spatial/fs time scale.
• That is the story I will tell today, and it prompted me to borrow the sub-title of Feynman’s 1959 lecture, widely viewed as a harbinger of the field of nano-technology. For those not familiar with Feynman’s lecture…

## Slide 2
I would like to describe a field [that]
… would have an enormous number
of technical applications: the problem
of manipulating and controlling things on a small scale....
Why cannot we write the entire 24 volumes of the Encyclopedia
Britannica on the head of a pin?
... all it is necessary to do is to reduce in size all the writing in the
Encyclopedia by 25,000 times.... A period would contain 1000 atoms.
There’s Plenty of Room at the Bottom
Jefferson 6 GeV Accelerator Lab
Texas 2 GeV
accelerator
Klystron hall
WPE:
~0.1
continuous
~ 10-4 A
e-beam
one
< 10 fs,
0.1 nC
bunch/hr
(104 A peak;
10-13 A avg)
WPE:
< 10-7
1 foot
Texas PW Laser
Notes: … here are a few of its key passages that are relevant to the subject at hand.
• Jefferson Lab: WPE ~0.1, continuous 200 µA beam
• TPW-LPA: WPE < 1e-7, one ~10 fs, 0.1 nC bunch/hr (< 1e-7 µA)

## Slide 3
GeV Laser-Plasma electron accelerators are poised to transform biology, chemistry and physics
by putting table-top femtosecond X-ray free-electron lasers in every major research university
Particle accelerators have evolved into the 21st century’s
most powerful* scientific instruments
* and largest and most expensive
TeV:
GeV:
MeV:
CERN-LHC
Membrane protein Photosystem I
Chapman et al., Nature 470, 73 (2011)
cyclotron
patient
magnets
gantry
undulator
3 km
linac
2 km
injector
x-ray optics
Experimental
hall
$6 B
$0.5 B
$0.2 B
Laser proton accelerators are poised to miniaturize cancer therapy…
Jung, PRL 107, 115002 (2011)
…and ignite fusion
Fernandez, Nucl. Fus. 49, 065004 (2009)
Laser
MeV protons
Target
H-rich film
e- cloud
Notes: Make point about table-top x-ray sources and their importance for science on this slide.
Jung, PRL 107, 115002 (2011) – recent proton acceleration results
Fernandez, Nucl. Fus. 49, 065004 (2009) – ignition of laser fusion

## Slide 4
Tajima
Dawson
Helium Gas Jet
Electrons Accelerating on a Laser-Driven Plasma Wave
Laser Pulse Focuses
Ionize Gas & Make Wave
Gas Jet Fires
Wave Captures and
Accelerates Electrons
0.1 to 10 cm
Tajima & Dawson, Phys. Rev. Lett. 43, 267 (1979)
4x1018 cm-3
2x109 V/cm
ne0
trapped e-
δn
laser
pulse
plasma wave
ne
z
Accelerating Field:
0.7x109 V/cm
5x1017 cm-3
~105 V/cm
(conventional accelerators)
4x1018 cm-3
Acceleration Length:
5x1017 cm-3
0.5 cm
9.5 cm
>105 cm
(conventional GeV accelerators)
PW peak power needed to self-guide and
self-inject at < 1018 cm-3 plasma density
1 GeV
7 GeV
1 GeV
7 GeV
externally
injected
“hadron”
self-injected
“electrons”
Notes: Laser pulse duration chosen to excite plasma wave RESONANTLY.

## Slide 5
Today, most LPAs operate in the “bubble” regime…
Before 2004:
After 2004:
Leemans, Nat. Phys.(2006)
Energy Gain (MeV)
1000
500
0
250
500
0
pC GeV-1
sinusoidal wake
Review: Esarey, Rev. Mod. Phys. 81, 1229 (2009)
E = 1 GeV
∆E/E = 5 %
θdiv = 5 mrad
Q ~ 0.1 nC
tbunch < 10 fs
Ipeak ~ 100 kA
... because point-like injection enables quasi-monoenergetic acceleration
0
5
10
electron density (1018 cm-3)
Kalmykov (2009)
x = 0 mm
Kalmykov (2009)
x = 0.3 mm
Kalmykov PRL (2009)
x = 0.6 mm
plasma bubble
Pukhov and Meyer-ter-Vehn, Appl. Phys. B 74, 355 (2002)
Geddes, Nature (2004)
Faure, Nature (2004)
Mangles, Nature (2004)
Ishay Pomerantz, “An
ultra-short pulsed neutron
source,” AMO Seminar,
Oct. 11, 2013
Notes: Lead-in: One of the most important discoveries along the 20-year path to mature TW-LPA was that the quasi-linear sinusoidal waves depicted in the previous slide produced electrons with wide energy spread, because of the difficulty of injecting electrons into the wave with sub-plasma-wavelength precision.
• In 2004, we learned that a highly nonlinear regime in which the drive pulse creates an electron density “bubble”, in a remarkable act of self-organization, gives rise to highly mono-energetic electrons up to 1 GeV in energy, as depicted here.

## Slide 6
The bubble regime offers trade-offs in de-
signing multi-GeV LPAs – e.g. pulse duration
Wei Lu et al., Phys. Rev. Special Topics - Accel. & Beams 10, 061301 (2007)
“Generating multi-GeV electron bunches using single stage laser wakefield acceleration in a 3D nonlinear regime”
τ = 30 fs, 1 PW pulse
τ = 150 fs, 1 PW pulse
Greater pump depletion length Lpd
1018
1017
1019
Plasma density ne [cm-3]
30 fs
Pump depletion
length [cm]
1
10
100
150 fs
unstable
(Texas PW)
(all those other guys)
… but within that broad limit, we have choices:
Pulse duration (ωpτ < 1)
is necessary to avoid
Raman instability …
~
Notes: Lead in to next slide with: “Now, putting together the accelerating field, dephasing and pump depletion lengths, and options regarding pulse duration and guided a0, we arrive at a plot of accelerated electron energy vs. plasma density…”

## Slide 7
1
10
100
1018
1017
1019
I
Plasma density ne [cm-3]
ωpτ: 0.2  1
Wang
(2013)
“Short Pulse PW”: τL ~ 30 fs, EL ~ 30 J
• plasma channel guiding (best near 1018 cm-3)
• up to 1 pulse/s
• limited to < 10 GeV by pump depletion
“Long Pulse PW”: τL ~ 150 fs, EL ~ 150 J
• self-guiding
• 1 pulse/hour
Two complementary INITIAL approaches to PW, multi-GeV
laser-plasma acceleration are emerging
SLAC
• theoretically capable of ~30 GeV
Previous TW
LPA
experiments
(1992-2012)
Electron energy gain ∆W [GeV]
Texas PW
Texas PW theoretical limit
Short-pulse PW theoretical limit
(plenty of room for improvement
“at the bottom”)
Notes: Lead-in: Putting together the considerations of the previous slides, energy gain ∆W is inversely proportional to plasma density ne, with a band of possibilities determined by pulse duration (i.e. pump depletion length) and guided intensity a0.
Previous TW experiments had to be conducted at ne > 2e18 cm-3, for the reasons discussed, and were therefore capped at ∆W ~ 1 GeV.

## Slide 8
OUTLINE
1) Initial 2 GeV PW-laser-driven e- acceleration results
2) How do we improve upon these results?
3) Wider vision of plasma-based accelerators
• robust plasma channels at ne ~ 1017 cm-3
• specialized injection techniques yielding ∆E/E < 1%
• 4D single-shot laboratory visualization of laser wakes
• highest LPA energy to date
• lowest beam divergence (< 0.5 mrad) from an LPA
• lowest plasma density (ne ~ 3e17 cm-3) for an LPA

## Slide 9
Experiments at the Texas Petawatt Laser aim to produce
quasi-mono-energetic multi-GeV e- beams in one 10 cm stage
Lower ne (1017 vs 1019 cm-3): longer dephasing (Ld) & pump depletion (Lpd) lengths
Longer interaction (8 cm gas cell vs < 1 cm jet): to exploit longer Ld and Lpd
Longer τpulse (150 fs vs < 60 fs): to excite plasma waves resonantly
Higher peak power (~ 1 PW vs < 0.18 TW): to self-guide, create plasma bubble,
trigger self-injection at low ne
Kalmykov et al., New J. Physics 12, 045019 (2010)
KEY DIFFERENCES FROM PREVIOUS EXPERIMENTS:
“Numerical modeling of multi-GeV laser wakefield accelerator driven by self-guided petawatt pulse,”
100

## Slide 10
E. Gaul et al., Appl. Opt. 49, 1676 (2010)
f/40
Wakefield
The Texas Petawatt Laser delivers 1.05 µm,
150 fs pulses up to 150 J on target
150 fs = 1 plasma oscillation
period at ne = 3•1017 cm-3
150 J = muzzle energy
of .22LR caliber
pistol bullet
Final mixed glass amplifier from NOVA
Notes: Mention that only ≤100 J used so far in experiments.
BELLA:
• 300 m^2 (laser) + 80 m^2 (target bay) • single-purpose facility • up to 1 Hz • 40 fs, 40 J • high Strehl ratio • “world’s most powerful laser”
TPW:
• 200 m^2 (laser) + 50 m^2 (target bay) • multi-purpose facility • 1 pulse/hour • 150 fs, 150 J • low Strehl ratio (currently)* • “world’s most powerful laser”
* So energy coupled into plasma is probably about the same as with BELLA.

## Slide 11
≤ 120 J 150fs
CCD
Al deflector
IPHS IPHR
Tungsten wire fiducial arrays
optical filters
gas cell
vacuum
laser
polarization
laser
electrons
magnet
Experimental setup emphasizes high precision & redundancy in e- energy measurement up to 2 GeV
1.1 T
6.7 cm
IPLE
Scale drawing of magnetic spectrometer:
x-rays
Beam
dump
pressure sensor
θ [mrad]
Energy [GeV]
2.0
1.0
2.0
-2.0
scintillators
Energy [GeV]
Deflection from axis [cm]
0
θ [mrad]
20
10
2.0
0.5
1.0
5
-5
x-rays
electrons
Raw IP data
fiducial shadows
1.9
2.0
2.1 GeV
0.8
0.6
0.4
0.2
0
Probability
2σ
2.0 GeV ± 5% (2σ)
x-ray source
magnet
2.0 m
1.0 m
0
2.5 m
IP
CCD
Notes: Here is a schematic diagram of the experiment. In our diagnostics, our goal was to build redundancy into our diagnostics.
TPW laser pulse enters gas cell
-> show laser focal spot
2) The actual focal spot was typically far from a gaussian, having multiple hot spots,
3) the gas cell is filled with He
-> show pressure sensor and comment on pressure in the gas cell just before and after the pulse arrival
4) it creates and then interacts with the plasma
-> show side-scatter image
5) RSFs, creates bubble, is guided, self-injection and acceleration of electrons take place
6) the laser pulse is sent to a beam dump by a thin Al deflector placed in its path
6) and the self-injected and accelerated electrons leave the gas cell, enter a magnetic spectrometer, are deflected by it. Low energy electrons are recorded on an imaging plate not from the magnet,
-> show raw high-E IP picture
7) and the high-energy one (> ~350 MeV), as well as the betatron x-rays, traverse the diagnostic chamber and reach the end of the chamber where they are recorded on a double layer of imaging plates (quick comment of HS, HR?).
-> show Lanex/scintillator images
8) The energetic electrons leaving the IP arrive at a Lanex + scintillator double layer forming the exit to the diagnostic chamber, and the light from both is collected by CCD.
show
9) We placed thin W wires in the path of the electrons (focus on wire arrays);
-> show fiducial arrays and electron trajectories
10) analyzing the shadows made by the wires on the imaging plates made it possible, by a process of triangulation, to locate the source of the x-rays within the gas cell and deconvolve electron launch angle and its energy in order to determine the electron energy spectrum.
-> point to side-scatter image and the x-ray position
11) This analysis revealed that the x-rays originate within the last 2 cm of the gas cell.
-> show the delta E/E value at 2-sigma
12) Our energy calibrations have an accuracy of +- 5% at 2 GeV (ask Rafal to explain his work in gory detail)

## Slide 12
Electron Energy [GeV]
Angle [mrad]
betatron
x-rays
pC/GeV-sr
GeV
Angle [mrad]
We observe quasi-mono-energetic peaks up to 2 GeV
• narrowest divergence (< 0.5 mrad)
• lowest density
Angle [mrad]
vertically integrated
electron spectra
(PSL)
high-energy
tails
10% (raw)
5% (actual)
65
pC
8% (raw)
4% (actual)
35
pC
15
pC
low-energy
electrons
GeV electrons
1.5 – 2.0 GeV shots reproduced many times!
Wang et al., Nature Commun. 4, 1988 (2013)
self-injected LPA observed
down to 1 x 1017 cm-3
• highest energy (2 GeV)

## Slide 13
Betatron x-rays: electrons wiggle while accelerating
Cu
mask
Al
mask
2 mm
0.25 mm
W wires
Rousse, PRL 93, 135005 (2004); Kneip et al., Nature Phys. 6, 980 (2010); Cipiccia et al., Nature Phys. 7, 867 (2011)
Kneip et al.
from 200 MeV LPA
(106 – 108 photons)
108 - 109 photons
25 ± 10 keV r.m.s.
Cipiccia et al.
from 700 MeV LPA
with resonant enhancement

## Slide 14
OUTLINE
1) Initial 2 GeV PW-laser-driven e- acceleration results
2) How do we improve on these results?
3) Wider vision of plasma-based accelerators
• robust plasma channels at ne ~ 1017 cm-3
• specialized injection techniques yielding ∆E/E < 1%
- density downramp injection
- ionization-induced injection (I3)
- colliding pulse injection
* 4D single-shot laboratory visualization of laser wakes
• highest LPA energy to date
• lowest beam divergence (< 0.5 mrad) from an LPA
• lowest plasma density (ne ~ 3e17 cm-3) for an LPA

## Slide 15
Current 7 cm
diameter
deformable
mirror (DFM)
Learning to manage the non-ideal mid-field focus profiles
of big laser systems may improve self-guiding
Planned ~25 cm
diameter DFM
Focus diagnostic &
correction system:
typical non-Gaussian
amplified laser profile,
fills gain medium
Strehl ~ 0.3
: ~10 cm
actual path: ~3 cm

## Slide 16
Spence, Phys. Rev. E 63, 015401 (2001): Butler, Phys. Rev. Lett. 89, 185003 (2002)
ne is minimum, and refractive index
maximum, on the waveguide axis.
Current Challenges:
• achieve 1017 cm-3 axial density reliably
• shape radial profile to control guided a0
• avoid wall damage at PW power
• taper longitudinally to enhance Ld
Leemans et al., Nature Physics 2, 636 (2006)
Essential to optimizing 30 TW LPA!
Gas-filled capillary discharge waveguides
extend acceleration length
Oxford U.
Simon Hooker group
ne ~ 1018 – 1019 cm-3

## Slide 17
Bobrova et al., Physics of Plasmas 20, 020703 (2013)
1) Laser-heater assisted capillary discharge waveguides.
New capabilities in low-ne plasma waveguides are emerging
2) Longitudinally tapered waveguide
increases wake phase velocity βp
and extends dephasing length Ld
ns laser
heater
• reduces ne on axis to ~ 1017 cm-3
• creates narrow, controlled guiding profile
• remote from walls, avoiding damage
Kim et al., APL 102, 204103 (2013)
1D MHD simulations
laser heater
laser
gas
sapphire channel
+V
0 V
ne(z)
z
laser group velocity

## Slide 18
Researchers are working on several approaches to CONTROL
localized injection into a highly nonlinear plasma wave.
3) Pre-accelerate quiescent “surfers”
in the plasma sea
(colliding-pulse injection)
Slow the wave
momentarily
(density down-ramp injection)
dne/dz < 0
2) Create moving “surfer”
within the wave
(ionization-induced injection)
Notes: Remind audience that the difficulty of injection is a primary reason that low n_e, multi-GeV LPA was not done earlier.

## Slide 19
Nitrogen K-shell electrons inject & trap
Pak, PRL 104, 025003 (2010)
2-stage injector-accelerator can improve beam quality
Pollock, PRL 104, 045001 (2011)
2-stage gas cell
pure He
He + N2
[MeV]
Plasma:
ne = 3 x 1017 cm-3 (He)
with 1% N2 dopant
Laser:
90 J, 150 fs,
f/40 focus
Result of test shot at Texas PW
~1% N2 doping of He plasma enables
Ionization-Induced Injection (I3)
simulation courtesy Austin Yi

## Slide 20
differentially pumped He gas cell
150 J, 150 fs, f/# ~ 40
Texas Petawatt Pulse:
0
5
10
z [cm]
Self-injected multi-GeV
accelerated electrons
to
detectors
Its structure & dynamics are too important
to leave entirely to theoreticians!
Kalmykov et al., “Electron self-injection and trapping into an evolving plasma bubble,”
Phys. Rev. Lett. 103, 135004 (2009)
laser pulse focuses,
bubble created
laser pulse defocuses,
bubble expands
laser pulse &
bubble guide
2
4
6
8
10
0
1
3
# electrons [arb.]
Energy [GeV]
electrons accelerate quasi-monenergetically to ~10 GeV
Plasma bubble
& laser profiles:
electrons inject
To realize the accelerator’s full potential,
we must learn to SEE it in the laboratory
The plasma “bubble” serves 4 functions:
1. cathode
4. accelerator
2. laser waveguide
3. electron collimator

## Slide 21
Nicholas Matlis
PhD 2006
Ionization
Front
Chirped
Reference
Pulse
Chirped
Probe
Pulse
Pump
Pulse
“Frequency Domain Holography” Images Wakefields in a Single-Shot
Fixed Delay
CCD
grating
imaging
optics
mirror
imaging
spectrometer
Null HOLOGRAM
Signal HOLOGRAM
Wavelength [nm]
50
-50
0
50
-50
0
distance [µm]
390
400
410
405
395
(now a Research
Scientist at LBNL)
N. Matlis et al., “Snapshots of laser wakefields,” Nature Physics 2, 749 (2006)
Laser wake
modulates probe
phase & amplitude
(FM & AM)
Notes: probe illuminate whole object, just like object beam in conventional holography, advanced ref pulse becomes analogue of ref beam in conv. holog, interfere with eachother in recording device which in this case is the CCD of the spectrometer. Because interference happens in spectrometer, we call it frequency domain holography…
To address these issues, we developed a modification to FDI called Frequency Domain Holography, or FDH, capable of measuring temporally-varying features in a single shot. The essence of this modification is to replace the short probes with temporally-long ones that experience phase-shifts from different parts of the wakefield simultaneously. In this experiment the temporally-long probes are generated by chirping (click) the originally short second-harmonic probe pulses to about 1 ps. The chirped probes are relay-imaged onto the slit of an imaging spectrometer where they interfere. The relay imaging provides spatial resolution in the transverse dimension, which is ultimately critical for reconstructing the spatially-varying features of the wakes. As can be seen by this sample raw data, the hologram shows considrably more complexity and thus information than the FDI interferograms which showed a simple overall phase shift.

## Slide 22
P. Dong et al., “Holographic Visualization of Laser Wakefields,” New Journal of Physics 12, 045016 (2010).
Experiment
Simulation
Wakefield snapshots see laser-plasma acceleration physics in unprecedented detail
60
∆ϕprobe(r,ζ)
0.4
ne(r,ζ)
0
ζ [ps]
0
60
r [µm]
ζ [ps]
r [µm]
0
0.4
• relativistic wave front curvature
0
60
60
• peaks grow, narrow & break behind pump
pump

## Slide 23
no gas
1.2•1019
no electrons
no electrons
20
40
60
80
100
120
0
200
400
600
800
1000
time behind pump [fs]
electron energy [MeV]
3.2•1019
distance from propagation axis [µm]
reconstructed |Eprobe(r,ς)|
electron spectrum
unperturbed
probe
Probe amplitude [arb.u.]:
Electron density “bubbles” re-shape co-propagating
probe pulses into optical “bullets”,
allowing us to see & study them directly
bubble
forms
P. Dong et al., Phys. Rev. Lett.104, 134801 (2010)
2.6•1019
poly-
energetic
electrons
elongated
bubble
mono-energetic
electrons
compact
bubble
30 TW pump
Optical bullet
SIMULATIONS
of bubble
0
4
8
EXPERIMENTS
30 TW pump
Peng Dong
PhD 2010
(now at UC-
San Francisco)

## Slide 24
Frequency-Domain “Streak Camera”
Records EVOLUTION of Plasma Bubble
in ONE shot
• Phase streak is a temporal sequence of the object’s projections
• We can record several of them simultaneously to recover
the object’s evolving structure tomographically
phase streak
Z. Li et al., Opt. Lett. 35, 4087 (2010)
Research Highlight, Nature Photonics 5, 68 (2011)
Zhengyan Li

## Slide 25: Frequency-domain tomography (FDT) records multiple phase streaks in one shot…
λprobe [nm]
lens
cascaded
4WM
lens
800 nm
pump
spectrometer
400 nm
probes
400 nm
ref. pulse
800 nm
probe
gener-
ators
CCD
1) 2D Hologram
2) Reciprocal 2D Hologram
FT
3) Phase Streaks
glass
ϕ = 1o
ϕ = 27o
ϕ = -25o
ϕ = -65o
ϕ = 68o
window
and IFT
4) Tomographic
Reconstruction
medical CT

## Slide 26: Single-shot tomographic movies help unravel the complex physics of filament formation in Kerr media
self-guided filament
PUMP
PULSE
ENERGY
Propagation distance zob into medium
Time from peak of pump pulse
nonlinear
refractive
index ∆n
linear propagation
mild self-focusing
strong self-focusing
arrested collapse
self-guided filament formation
plasma generation
Single-shot movie
xob [µm]
0.7 µJ
0.6 µJ
0.5 µJ
0.4 µJ
ζ [fs]
Zhengyan Li 2014
Best Technical Short Subject

## Slide 27
We have fielded a probe line at the Texas Petawatt
Laser to visualize plasma bubble dynamics directly
1
2
3
4
5
6
laser
bubble
phase streak
of plasma
bubble
appears as
side scatter
disappears
Plasma seminar,
Friday
October 25:
Zhengyan Li,
“Single-shot
visualization
of laser-plasma
Interactions”

## Slide 28
OUTLINE
1) Initial 2 GeV PW-laser-driven e- acceleration results
2) How do we improve on these results?
3) Vision of future LPA-driven x-ray FELs
• high PW beam quality
• robust plasma channels at ne ~ 1017 cm-3
• specialized injection techniques yielding ∆E/E < 1%
• 4D single-shot laboratory visualization of laser wakes
• long pulse PW (Texas)
• short pulse PW (LBNL)
• table-top x-ray FELs
• electron/proton-beam-driven plasma electron accelerators
• laser-plasma proton/ion accelerators

## Slide 29
2
10
1 PW, 150 fs
2
E = 2 GeV
∆E/E = 0.1 %*
0.1 π mm-mrad
tbunch = 10 fs
Ipeak = 100 kA
Possible with demon-
strated LPA capability
* improvements over existing capability
from Altarelli, European X-ray FEL (DESY Tech. Rpt)

## Slide 30
3.2 km
Stanford Linear Accelerator Center
42 GeV
84 GeV
Drive e beam
Plasma
ions
Accelerating
beam
Nonlinear “bubble” or “blowout” regime
Facility for Advanced
Accelerator Experimental
Tests (FACET) uses SLAC
injector and 2/3 of linac to
deliver compressed 25 GeV
e- and e+ drive bunches and
synchronized accelerating
bunches.

## Slide 31
Nature Physics 5, 363-367 (2009)
proton driver:
• 1 TeV
• 1011 protons
• σz = 100 µm
• σx,y = 0.43 mm
• σθ = 0.03 mrad
electron witness
bunch:
• 10 GeV
• 1.5 x 1010 e-
plasma:
• ne = 6 x 1014 cm-3
• λp = 1.35 mm
• L = 600 m
• nonlinear “blowout”
regime
• Ez ~ 2 GeV/m
e-
bunch
proton
bunch
0 m
150 m
300 m
450 m
A potential plasma path to
the energy frontier and the ILC

## Slide 32
virtual
cathode
protons
Hydrogen-rich
film
Laser
pulse
Ez ~
kThot
λDebye
~ 1010 V/cm
initial accelerating field:
• Needed for clinical therapy:
~ 200 MeV, same energy,
tunable
Monoenergetic protons precisely
expose small volumes within the
body  no side effects
Haberberger, Nat. Phys. 8, 95 (2012)

## Slide 33
Yes, there’s plenty of room --- and plenty of food ---
at the bottom
bottom feeder
2 GeV
Graduate Students:
• Stefan Bedacht (MS 2009)
• Yen-Yu Chang
• Peng Dong (PhD 2010)
• Dongsu Du (MS 2010)
• Neil Fazel
• Rick Korzekwa
• Spencer Jolly
• Zhengyan Li (Oscar 2014)
• Nicholas Matlis (PhD 2006)
• JC Sanders
• Joey Shaw
• Hai-En Tsai
• Austin Yi (PhD 2012)
• Xi Zhang
Postdocs & Senior Scientists:
• Watson Henderson
• Serguei Kalmykov
• Vladimir Khudik
• Chih-Hao Pai
• Xiaoming Wang
• Rafal Zgadzaj
Financial Support:
• U.S. Department of Energy
• U.S. National Science Foundation
Collaborating Faculty:
• Todd Ditmire
• Mike Downer
• Gennady Shvets
Texas Petawatt Laser Staff:
• Aaron Bernstein
• Ted Borger
• Mike Donovan
• Gilliss Dyer
• Erhard Gaul
• Mikael Martinez
• Hernan Quevedo
• Michael Spinks

## Slide 34
Neil
Fazel
Rafal
Zgadzaj
Xiao-
ming
Wang
Watson
Henderson
Zhengyan
Li
He
gas
Acknowledgements
Interaction chamber
e-
diagnostics
• Texas LPA team:
U. S. Department of Energy
U. S. National Science Foundation

## Slide 35
END